|  | OAQ SOURCE SPECIFIC OPERATING AGREEMENT OA-13: External Combustion Sources (326 IAC 2-9-13) State Form 53450 (R / 1-10) INDIANA DEPARTMENT OF ENVIRONMENTAL MANAGEMENT | IDEM – Office of Air Quality – Permits Branch 100 N. Senate Avenue, MC 61-53 Room 1003 Indianapolis, IN 46204-2251 Telephone: (317) 233-0178 or Toll Free: 1-800-451-6027 x30178 (within Indiana) Facsimile Number: (317) 232-6749 www.IN.gov/idem |
| --- | --- | --- |
| NOTES: | The purpose of this form is to identify all of the source specific operating agreement requirements for 326 IAC 2-9-13. Detailed instructions for this form are available on the Air Permit Application Forms website. Rule specific definitions are listed in 326 IAC 2-9-13(a) for boiler, dryer, oven, process heater, space heater, and water heater. All information submitted to IDEM will be made available to the public unless it is submitted under a claim of confidentiality. Claims of confidentiality must be made at the time the information is submitted to IDEM, and must follow the requirements set out in 326 IAC 17.1-4-1. Failure to follow these requirements exactly will result in your information becoming a public record, available for any one to inspect and photocopy. |

| Part A: Source Description |
| --- |
| Part A identifies the source and describes the nature, design capacity, and typical operating schedule of the source. |
| Source Description: |  |
| Sourcewide Design Capacity (specify units of measure): |  |
| Operation Schedule: | hours per day days per week weeks per year |

Part B: Operating Agreement

Part B certifies that the operation qualifies for the source specific operating agreement.

Operating Agreement

I have reviewed the requirements under 326 IAC 2-9 and have determined that the proposed operation qualifies for a source specific operating agreement (SSOA) under this rule.

_________________________________________ ____________________________________________ Name (typed) Title _________________________________________ ____________________________________________ Signature Date (month, day, year)

Part C: Compliance Option

Part C identifies the option that source is choosing for compliance with the requirements of 326 IAC 2-9-13. Choose only ONE of the following options.

OPTION 1: I will comply with the requirements of 326 IAC 2-9-13 by carrying out the following set of requirements for any external combustion source, including any combination of boilers, space heaters, ovens, dryers, or water heaters.

Process Limitation: 326 IAC 2-9-13(b) (1) and (2)(A) Visible emissions from the source shall not exceed twenty percent (20%) opacity in twenty-four (24) consecutive readings in a six (6) minute period. The opacity shall be determined using 40 CFR 60, Appendix A, Method 9*. Limit fuel usage for every twelve (12) month period to less than the limits found in subsection (f), Table 1 for a single fuel or a combination of two (2) fuels.

Monitoring Requirements: 326 IAC 2-9-13(c) Sources must be able to demonstrate compliance no later than thirty (30) days after receipt of a written request by the department or U.S. EPA. No other demonstration of compliance shall be required. A source specific operating agreement is not required for these sources.

OPTION 2: I will comply with the requirements of 326 IAC 2-9-13 by carrying out the following set of requirements for any external combustion source, including any combination of boilers, space heaters, ovens, dryers, or water heaters.

Process Limitation: 326 IAC 2-9-13(b) (1) and (2)(B) Visible emissions from the source shall not exceed twenty percent (20%) opacity in twenty-four (24) consecutive readings in a six (6) minute period. The opacity shall be determined using 40 CFR 60, Appendix A, Method 9*. Limit fuel usage for every twelve (12) month period to less than the limits found in subsection (g), Table 2 for a single fuel or a combination of two (2) fuels.

Record Keeping Requirements: 326 IAC 2-9-13(e) The following records shall be kept at the source: (1) Hours operated for each combustion unit. (2) Records of annual fuel usage for each combustion unit. (3) Routine maintenance records.

This space is intentionally left blank.

| Part D: Fuel Limits |
| --- |
| Part D specifies the fuel limits associated with 326 IAC 2-9-13. |
| TABLE 1 [326 IAC 2-9-13(f)] |
| Fuel | Maximum Fuel Usage per Year |
| Single Fuel |
| Natural gas; Maximum capacity: 0.3 to <10 MMBtu/hr | 1,000.0 | MMCF |
| Natural gas; Maximum capacity: 10 to 100 MMBtu/hr | 714.0 | MMCF |
| Natural gas; Maximum capacity: >100 MMBtu/hr | 181.0 | MMCF |
| Fuel oil #1 and #2 (distillate) | 1,408.0 | kgals |
| Fuel oil #5 and #6 (distillate) | 181.0 | kgals |
| Liquified petroleum gas (LPG) | 5,263.0 | MMCF |
| Coal (bituminous and subbituminous) | 786.0 | tons |
| Bark-only | 5,882.0 | tons |
| Wood-only | 7,352.0 | tons |
| Wood and bark | 7,352.0 | tons |
| Dual Fuel |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: 0.3 to <10 MMBtu/hr | 976.0 117.0 | MMCF kgals |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: 10 to 100 MMBtu/hr | 697.0 117.0 | MMCF kgals |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: >100 MMBtu/hr | 177.0 117.0 | MMCF kgals |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: 0.3 to <10 MMBtu/hr | 1,407.0 83.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: 10 to 100 MMBtu/hr | 1,407.0 59.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: >100 MMBtu/hr | 1,407.0 15.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Fuel oil #5 and #6 (residual) | 1,291.0 15.0 | kgals kgals |
| Coal (bituminous and subbituminous) / Bark, wood, or wood and bark | 786.0 490.0 | tons tons |
| Bark, wood, or wood and bark / Coal (bituminous and subbituminous) | 5,858.0 65.0 | tons tons |

| Part D: Fuel Limits |
| --- |
| Part D specifies the fuel limits associated with 326 IAC 2-9-13. |
| TABLE 2 [326 IAC 2-9-13(g)] |
| Fuel | Maximum Fuel Usage per Year |
| Single Fuel |
| Natural gas; Maximum capacity: 0.3 to <10 MMBtu/hr | 1,600.0 | MMCF |
| Natural gas; Maximum capacity: 10 to 100 MMBtu/hr | 1,142.0 | MMCF |
| Natural gas; Maximum capacity: >100 MMBtu/hr | 290.0 | MMCF |
| Fuel oil #1 and #2 (distillate) | 2,253.0 | kgals |
| Fuel oil #5 and #6 (distillate) | 291.0 | kgals |
| Liquified petroleum gas (LPG) | 8,421.0 | MMCF |
| Coal (bituminous and subbituminous) | 1,258.0 | tons |
| Bark-only | 9,411.0 | tons |
| Wood-only | 11,764.0 | tons |
| Wood / bark | 11,764.0 | tons |
| Dual Fuel |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: 0.3 to <10 MMBtu/hr | 1,562.0 187.0 | MMCF kgals |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: 10 to 100 MMBtu/hr | 1,115.0 187.0 | MMCF kgals |
| Natural gas / Fuel oil #1 and #2 (distillate) Maximum capacity: >100 MMBtu/hr | 284.0 187.0 | MMCF kgals |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: 0.3 to <10 MMBtu/hr | 2,252.0 133.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: 10 to 100 MMBtu/hr | 2,252.0 95.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Natural gas Maximum capacity: >100 MMBtu/hr | 2,252.0 24.0 | kgals MMCF |
| Fuel oil #1 and #2 (distillate) / Fuel oil #5 and #6 (residual) | 2,065.0 24.0 | kgals kgals |
| Coal (bituminous and subbituminous) / Bark, wood, or wood and bark | 1,258.0 784.0 | tons tons |
| Bark, wood, or wood and bark / Coal (bituminous and subbituminous) | 9,373.0 104.0 | tons tons |